# Beginning to use the clockwork programming language
Martin Leadbeater, Sep 2013

This tutorial aims to show how clockwork can be used to explore some sample programs.

# Getting Started
The clockwork programming language is intended for monitoring and controlling systems and as such, clockwork programs normally run continuously. The distribution includes a small program: "hello.cw" that displays "Hello World" and then exits. The program script is:

Hello MACHINE { ENTER INIT { LOG "Hello World"; SHUTDOWN } }
hello Hello;

This following subsections aim to help you execute the hello.cw program.

## Install clockwork
- git clone http://github.com/latproc/clockwork
- cd clockwork/iod
- make -f Makefile.cw

## Run clockwork
- cd ../tests
- ../iod/cw hello.cw
The program will display a hello message:
2013-09-03 15:39:36.689 ------- hello: Hello World -------

# Using the interactive shell
Clockwork programs run continuously and it is possible to interact with them using a number of techniques:
- the interactive shell (iosh)
- the web user interface (to be covered later in this document)
- using ∅MQ (zeromq)
- using modbus
The simplest of these to start with is iosh.
## Starting iosh
- execute the steps in section 1.1, above; those step build 'cw' and 'iosh'
- run iod/iosh (if you are still in the clockwork/iod directory, simply type
  ./iosh
You should see a prompt like the following:

Connecting to tcp://127.0.0.1:5555

Enter HELP; for help. Note that ';' is required at the end of each command
  use exit; or ctrl-D to exit this program

1. enter HELP; to display a list of available commands
2. in another terminal, run clockwork against one of the test files in the clockwork/tests directory:

   ./cw ../tests/blink.cw
3. back in iosh, enter LIST; to display a list of machines that the clockwork program is running;

   > LIST;	type this
   blinker Blinker	clockwork responds with this

Look at the source for the blink program:
1	Blinker MACHINE {
2	on STATE;
3	off STATE;
4	ENTER on { WAIT 1000; SET SELF TO off; }
5	ENTER off { WAIT 1000; SET SELF TO on; }
6	}
7	blinker Blinker;
Note that the machine has two states, 'on' and 'off' the two ENTER functions cause the machine to flip between on and off after a delay of 1000ms.
you can also describe the internals of the blinker machine:
1	> DESCRIBE blinker;
2	> ---------------
3	blinker: INIT
4	Class: Blinker instantiated at: blink.cw line:10
5	properties:
6	NAME:blinker,STATE:INIT
7
8	Timer: 24503
From this description you can see that the machine called 'blinker' is in a state 'INIT' (line 3), also, blinker has been in the INIT state for 24.503 seconds.
When clockwork starts running, all machines enter a state called INIT. Normally they quickly change state automatically but since the 'blinker' has nothing that causes a state change to 'on' or 'off', it will stay in INIT forever.
manually set the blinker into the 'on' state using the SET command in iosh:
> SET blinker TO on;
you can also get the state of the blinker using the GET command:
> GET blinker;
> on
> GET blinker;
> off
Note: If the iosh command prompt '>' does not come back, iosh is trying to connect to an instance of clockwork but can't; check that you still have cw running on the local host.